## Slide 1: System Verilog Stopwatch
Waseem Orphali
Antonio Jimenez
Pengfei He
Devon Stedronsky
Notes: WO

## Slide 2: Agenda
Overview
Planning
Specification and Requirements
Module Development
Functional Verification
Lifecycle Data
Project Insights
1
2
3
4
5
6
7
Notes: WO

## Slide 3
Overview
Notes: WO

## Slide 4: Overview
Project Purpose
  Implement RTC Stopwatch project using System Verilog
  Implement DO254 standards documentation
  Implement project planning and version control standards
Project Scope
  Documentation and traceability meeting DO254 standards
  Version control using gitflow branching strategy
  Project management using Jira
  Implement RTL code to Xillinx Artix-7 FPGA board
Notes: WO

## Slide 5
Planning
Notes: PH

## Slide 6: Planning
Two phases were planned containing a total of nine stages to complete the project
Phase 1 (Preparation): Deadline
  Planning and Organization ------------------- 06/05/2020
  Research and Functionality Description -- 06/10/2020
  Requirement Generation --------------------- 06/11/2020
Phase 2 (Development):
  Module Development ------------------------- 06/12/2020
  Module Verification ---------------------------- 06/16/2020
  Top Level Implementation -------------------- 06/17/2020
  Functional Verification ------------------------ 06/17/2020
  Synthesis and FPGA Implementation ------ 06/18/2020
  Final ------------------------------------------------ 06/18/2020
Jira Project
Notes: PH

## Slide 7: Tools Used
Project Management:
  Jira
Version Control:
  GitHub
Coding
  Notepad++
  Vivado's text editor
Simulation and Implementation
  Xilinx Vivado Design Suite
  Nexys A7100T development board
Notes: PH

## Slide 8
Specifications and Requirements
Notes: AJ

## Slide 9: System Specification
100Mhz system clock input
Active low reset
Trigger input button controls start/stop/resume
  7-segment display shows time elapsed
    Format – MM:ss:mm
  Display rolls back to 00:00:00 after one hour
Five submodules
  Trigger detection
  Timer (clock divider)
  Counter
  7 Segment
    BCD data conversion
    Display adapter
Notes: AJ

## Slide 10: Trigger Detection Requirements
Disables Counter and timer module when active low signal is sent to i_reset_n
Initializes counter module when an active low signal is sent to i_reset_n
Enables/Disables counter and timer module when rising edge is sent to i_trigger
Debounces the signal sent to the i_trigger input
Notes: AJ

## Slide 11: Timer Requirements
Initialization
  Internal counter is set to value of 1
  Output 'o_basetick' outputs 0
  Maximum value of counter 'MAX_COUNT' is 500000
Timer-Enable
  Timer module takes 100 Mhz clock as input and outputs a 100 Hz clock
  Internal counter increments by 1 on the rising edging of 'i_sclk' when 'i_timerenb' and 'i_reset_n' are 1
  Output 'o_basetick' is toggled when counter reaches MAX_COUNT and internal counter is reset to 0
Timer-Reset
  Internal counter is set to value of 1
  Output 'o_basetick' outputs 0
Notes: PH

## Slide 12: 24-bit Counter Requirements
4-bit BCD counter submodule
  Low-active reset and initialization conditions
  Parameterizable rollover count and flag output controls the maximum count allowed
  Increments on the rising edge of 'i_rtcclk' when 'i_countenb' and 'i_latchcount' are set to 1
  Output 'o_bcdcount' outputs the current value of the counter
    System Verilog allowed the module to use the output directly instead of using internal signals
24-bit BCD counter module
  4-bit BCD counter submodules are instantiated for each display digit
    Each instance takes the less significant digit's rollover flag as its input clock
    The least significant digit takes the 10ms timer output as the input clock ('o_basetick')
    Digits rollover at counts of 9 or 5 depending on the digit being displayed
  Output 'o_count' combines all instance outputs to a single bus
Notes: DS

## Slide 13: 7 Segment Display Requirements
Takes 24-bit BCD input coming from the counter
Splits the input BCD to six separate digits
Converts each BCD digit into its corresponding 7-segment display code:
  0 => 11000000
  1 => 11111001
  2 => 10100100
  3 => 10110000
  4 => 10011001
  5 => 10010010
  6 => 10000010
  7 => 11111000
  8 => 10000000
  9 => 10010000
Notes: WO

## Slide 14: 7 Segment Adapter Requirements
Takes in the six digits coming from the 7-segment display module, each represented as 7-segment code
Module keeps all segments and digits turned on when reset is active
Enables every digit on the display for
one millisecond at a time by enabling
the anode connected to the specific digit
Takes a total of six milliseconds to cycle
through the six digits being used
Notes: WO

## Slide 15
Module Development
Notes: WO

## Slide 16: Module Development
Submodule based design
  Concurrent development aided by version control
  I/O and internal signals defined by specifications and requirements
  All source files developed following defined coding standards
Each submodule was developed independently
  Preliminary testing was done to ensure compiling before pushing to working branch
  A separate team member developed test cases and functional verification of each module
Top level source file development was not blocked by module development
  Detailed requirements and specifications allowed for delays in module development while still generating code for the top-level implementation
Notes: WO

## Slide 17
Functional Verification
Notes: PH

## Slide 18: Test Bench and Module Verification
Each team member created test cases and a test bench for other team member's module
  Each module's original owner reviewed test cases and the test results for their module
    Reviews and edits to the documentation were committed to feature branches before the final versions were merged to the develop branch
Test cases are traceable back to their parent requirement as per requirements standards
  Test case tags are directly referenced in test bench console outputs
  Each test case was tested with a separate procedure, usually separated in the testbench by resetting the DUT module
  The test cases document for each module was updated with:
    Pass/Fail and actual results
    Git commit tag corresponding to the last edits made to the source files when debugging
Two methods of testing were used as necessary:
  Assert statements in the testbench and displaying the test result in the TCL console
  Observing the simulation waveform
    TCL console output indicates the expected time and output data for each test case
Notes: PH

## Slide 19
Lifecycle Data
Notes: AJ

## Slide 20: Sprint Burndown Charts
Notes: AJ

## Slide 21: Lifecycle Data
HDP and Joint Milestones
Schedule
Standards
Specifications
Requirements
Requirements Review
Test Cases
Test Case Review
Module Verification Review
Test Results
Notes: AJ

## Slide 22: GitHub Statistics
1830 lines of code in final release
  Source files and testbenches
134 total commits to master branch
  2 release branches
  25 merged pull requests
  67 unique commits
82 unique cloners
GitHub Repository
Notes: DS

## Slide 23
Project Insights
Notes: DS

## Slide 24: Insights
GitHub management
  Add commit naming conventions to configuration standards
  More restriction on merging to working branch
    Squashing commits
  Separating documentation and coding feature branches
Jira Project Management
  Using Jira on a smaller time scale to better manage schedule and task changes
  More granularity in workload assignment
  Documentation tracking and change requests
High-level system requirements
  Unable to verify exhaustively
Notes: DS